Light Arcade
Scott James
floridaconsulting@gmail.com
Github.com/scottjames

---
Game Idea
- Build a simple/fun 2-player game
  Entry for Maker Faire Orlando
- Short/Fast games, quick turn around
  No player lines, easy to observe
- No skill: Just hit buttons fast
- Countdown clock to add pressure to players
  10 seconds per game.

---
Approach – Hardware Build
- Use new methods and materials
  not PVC and plastic boxes
- Used 4" ECT, MDF custom milled
- Paint with "hammered" for industrial look.
- High impact display - stand out in a crowd
  not just another video game
- Portable (able to take to Maker Faire)

---
Approach – Electronics Build
- Simple, DIY electronics
- No custom fabricated PCB
- Use Vero Strip-Board
  Easier for people to copy/hack their own.
- High impact display - stand out in a crowd
- Use LED lights, not classic “video” game.
- Portable

---
Design
Use Arduino, much as possible
Raspberry Pi for multi-media display
Data feed to Pi is *receive only* (simpler)

---
Implementation
Platform: CPU board
Arduino pro mini (ATMega328, no USB)
Raspberry Pi, HDMI output to monitor
3-to-5 volt level shifter
Data flows from Arduino -> level shift -> Pi

---
Inputs
Inputs - buttons
Always did software debounce.
This time use hardware debouncing.
Research: 10 msec debounce period.
Utility buttons: start game, and ?
Multiple headers/pins to hook on and test inputs/outputs.

---
Display
NeoPixel display LED strips
Install LED inside buttons for feedback
VGA screen, Raspberry Pi

---
Arduino software
NeoPixel Library (adafruit.com)
Serial 115200 baud -> Pi data feed.
Serial text commands, easier debug/reading in terminal.
Event loop to drive game
State machine:
DEMO -> PLAY -> FINISH -> DEMO
Modular approach, Arduino-friendly, simple - Buttons - Game - Display - Serial
=

---
 Arduino software
NeoPixel display LED strips
Install White LED inside buttons for feedback
VGA screen, Raspberry Pi

---
Neo Pixels
- RGB LED (Worldsemi WS2812B chip)
- Individually addressable
- 24-bit color, 255 levels of brightness.
- Great for basic animation, color lighting.
- Not great for POV, video playback (too slow),
  newer WS2801/WS2822 can do 2-wire, 25MHz.
- 30 LED/Meter, 5 Meter roll: ~$30 (AliExpress)

---
Neo Pixels
Serial Data, like a bucket brigade.

---
Neo Pixels
- Not I2C,TWI or SPI – proprietary timing :(
  Use bit-bang to program.
- 1-bit cycle is about 1.2 microsecond.
- ~50+ usec frame (10 is ok)

---
[ Heart of Arduino ]
Atmel ATMega328
Features...
AVR risc cpu
UART (Serial I/O)
Gen. Purp. I/O
Flash (non volatile 32k)
Ram (8k)
Timer (3 total)
Analog → Digital

---
Main Board

---
Arduino: Pin Mapping
// === PIN CONFIGURATION ====================
#define PIN_P1B1 6 // btn 1
#define PIN_P1L1 7 // led 1
#define PIN_P1B2 8 // btn 2
#define PIN_P1L2 9 // led 2
#define PIN_P2B1 13 // btn 1
#define PIN_P2L1 12 // led 1
#define PIN_P2B2 11 // btn 2
#define PIN_P2L2 10 // led 2
#define PIN_NEWGAME 2 // util pin 2
#define PIN_PAUSE 3 // util pin 3
#define PIN_SELECT_POT A2 // voltage divider with Potentiometer to select game (someday)
#define PIN_STRIP0 A0 // strip0 / player 1
#define PIN_STRIP1 A1 // strip1 / player 2
// IMPORTANT: To reduce NeoPixel burnout risk, add 1000 uF capacitor across
// pixel power leads, add 300 - 500 Ohm resistor on first pixel's data input
// and minimize distance between Arduino and first pixel. Avoid connecting
// on a live circuit...if you must, connect GND first.

---
LightArcade Program
Modular Design:
LightArcadeSerial – main module
LAButton – button handler
LAGame – game “model”, “controller”
LAGraphics – LED display “view”
LASerial – Serial interface, text reports
Module common “methods”:
InitXXX()
updateXXX()

---
Arduino: Globals
// === MODULE GLOBALS ==============================
// store pin configuration in arrays for iteration later on
int pinLed[4] = {
     PIN_P1L1, PIN_P1L2, // Player 0 (Left/Blue)
     PIN_P2L1, PIN_P2L2 // Player 1 (Right/Red)
};
int pinButton[6] = {
     PIN_P1B1, PIN_P1B2, PIN_P2B1, PIN_P2B2, // P0, P1
     PIN_NEWGAME, PIN_PAUSE
};
int pinUtil[2] = { PIN_NEWGAME, PIN_PAUSE }; // utility inputs
// ~48" strip is 39 LEDs
#define NUM_STRIP_ELEMENTS 39
Adafruit_NeoPixel strip[2] = {
  Adafruit_NeoPixel(NUM_STRIP_ELEMENTS, PIN_STRIP0, NEO_GRB + NEO_KHZ800),
  Adafruit_NeoPixel(NUM_STRIP_ELEMENTS, PIN_STRIP1, NEO_GRB + NEO_KHZ800)
};
long now; // current millis, global clock
uint16_t x; // global loop counter for sequencing of lights, cycles 0 - 0xFFFF

---
Arduino: Setup()
void setup() {
  delay(2000); // delay at startup to power up
  // open fast serial port
  Serial.begin(115200);
  while (!Serial)
    ; // wait for serial port to connect. Needed for Leonardo only
  initButtons();
  // Some example procedures showing how to display to the pixels:
  Serial.println("# BEGIN SETUP");
  // setup strips and button LEDs; do lamp test.
  initGraphics();
  // setup new game
  initGameModel();
  x = 0;
  Serial.println("# END SETUP");
}

---
Arduino: Loop()
/**
 * Arduino loops with short period.
 * Only a couple calls are blocking (and they fix the clock)
 * Service Inputs, Game model, output to LED and Serial
 */
void loop() {
  now = millis();
  // service input buttons, debouncing and toggle delay values.
  updateButtons(x);
  // update game, calc button rate from toggle delay, calc player scores
  updateGameModel(x);
  // update display on led strips with current player scores
  updateGraphics(x);
  // send report to Raspberry Pi with: clockTick, button status, game state, etc.
  updateSerial(x);
  x++; // this global 16 bit unsigned integer will overflow (recycle) at 0xFFFF
// delay(5); // 5 msec sleep/tick interval
  delay(1); // 1 msec sleep/tick interval
}

---
Read Button
Buttons are active low (gnd == 0 == pressed)
// read 6 buttons, debounce, load into bitmask
// 76543210 = mask
// 1100 = player 0/1
// 1010 = button 0/1
// 32 = util aka Pi gpio 2,3
int readButtonsDebounce() {
  buttonCurrMask = 0;
  for (int b = 0; b < 6; b++) {
    buttonCurrMask |= ( (digitalRead(pinButton[b]) ? 0 : 1) << b ); // invert, LOW=1
  }
}

---
Button Logic (Toggle)
- Bit mask to read each button
- Detect on/off state comparing each loop
- Enforce toggle in bitmask
unsigned char toggleMask = 0x05;
// toggle bit mask for both pairs of buttons !MUST INIT 0x0101
// states for player0 (toggle with player0 ANDMASK = 0011 = 0x03)
// if btn0 on and toggleMask 0001, then toggleMask = 0010
// if btn1 on and toggleMask 0010, then toggleMask = 0001
// states for player1 (toggle with player1 ANDMASK = 1100 = 0x0c)
// if btn2 on and toggleMask 0100, then toggleMask = 1000
// if btn3 on and toggleMask 1000, then toggleMask = 0100
// XOR with toggleBit of 0x03 (btn0,1) or 0x06 (btn2,3)
int tryToggleButton(int btn, uint16_t x) {
  if ( (toggleMask & (0x01 << btn)) ) {
    // toggle the mask and wait for the other button
    // NOTE: btn & 0x02 is 0 for btn0,1 and is 1 for btn 2,3
    uint16_t player = (btn & 0x02) >> 1;
    uint16_t toggleBit = ( player ? 0x0c : 0x03 ); // player 1 ANDMASK=0x0c (0b1100), player 0 ANDMASK=0x03 (0b0011)
    toggleMask ^= toggleBit; // toggle both bits in mask with XOR
    toggleDelay[player] = (now - toggleTime[player]);
    // scale down delay, limit to MAX_DELAY
    toggleDelay[player] = ( toggleDelay[player] > MAX_DELAY) ? MAX_DELAY : toggleDelay[player];
    toggleTime[player] = now;
    //sendToggleReport(x); // DEBUG: send toggle report for testing...
    return true;
  }
  else {
    return false;
  }
}

---
Arduino Tour...
LightArcadeSerial

---
Pi Software
Need multi-media audio/video display
Easy to program/modify
Options?
Node.js
JohnnyFive robot api.
Python,
Pygame - perfect.
= IRL: problems... - button debounce too slow, tempo was important - some kids 'ran the table' as a result of learning tempo. - met game programmer "10 msec is glacial" - Serial slow way to pass data. - problems with time out of sync in Pi - had to turn off Pi in Orlando - Arduino work

---
Pygame (needs)
Slide Show – show pictures of build
Read serial data from Arduino
Event loop
Handle “reports” (no ACK required)
Demo: slides
Play: scores, countdown
Winner: show winner team

---
Pygame State Machine
Demo: show slides
Play: scores, countdown clock
Winner: show winner team

---
Pygame Programming
Serial – read text 'report' data stream
Canvas – display: Slides, Clock/Score, Winner
Sound – play 'start' and 'winner' sound
Tour pygame code...

---
Python Tour...
LightArcade.py

---
IRL: Button problems
Button debounce too slow
tempo was important
Worked ok...some kids 'ran the table' as a result of learning tempo.
Met game programmer at Maker Faire Orlando
"10 msec is glacial"

---
IRL: Data timing problems
To fix “score lag” last minute change...
Push toggleReport() on each button press.
toggleReport() overloaded python Serial buffer.
“finish” and sound had delay lag (out of sync).
Had to turn off Screen/Pi in Orlando :-(

---
It worked: fun time
Saturday: 10k people
Sunday: 4k people
Monday: lost voice

---
IRL: Connector problems
Pin Connector with RTV was flexible
acted as strain relief.
Added Sugru (looks great!)
Stiff connector had no strain relief, acted as fulcrum, pulled wire.
Solder joint broke (left blue LED strip)

---
LA++: next generation
Evolve the Game

---
LA++: design ideas
- offload LED strip display to dedicated Arduino
- New buttons, better LEDs for feedback
- Offload sound/clock (remove Pi dependency)
- Web cam with Pi / Open CV to capture player image at win/loss, like “Photo-Finish”
- Wi-Fi Portal / NoCatNet / Access Point

---
LA++: implementation ideas
 - I2C instead of Serial text; bus pirate
 - Serial used to flash Arduino, pain to disconnect.
 - I2C MP3 for sound? no Pi required.
 - I2C large 7-segment countdown.
I2C easy: using Wire.h in Arduino.
Arduino Tour... I2C...

---
Join us!
SuncoastMakers.org
- Hack Light Arcade, or make your own
- Other Ideas coming soon...
- Video Projection Mapping
- Computer Vision (OpenCV)
- Cicada POV (Stationary Fast LED Strips)